## Slide 1
Annex – Why the levy uses 0.718 and 0.440
CBAM prices imported electricity on the intensity of the exporter's fossil fleet, not on its grid average. The gap is a definition, not a penalty.
▪ The rule. Article 7(3) of Regulation (EU) 2023/956 sends imported electricity to default values; Annex IV §4.2.1 sets them at “the CO₂ emission factor in the third country”; Article 1(4) of IR (EU) 2025/2621 makes that Annex III.
▪ The definition that creates the gap. Annex IV §1(d) defines that factor as “the CO₂ emission data of the electricity sector” divided by “the gross electricity generation based on fossil fuels”. Hydro, nuclear and renewables are struck from the denominator.
▪ So the export default is the grid average divided by the fossil share. Not a penalty applied to the mix — a different denominator. Both annexes are five-year averages of IEA data (IR recitals 7 and 8), built on a deliberately conservative approach (recital 3).
▪ Goods use the other annex. For electricity consumed in producing steel or aluminium, IR recital 7 keeps the country grid average — Annex II. Same source, same years, different denominator.
 | Grid average Annex II | Export default Annex III | Implied fossil share of generation
Türkiye | 0.420 | 0.718 | 58 %
Georgia | 0.102 | 0.440 | 23 %
Ukraine | 0.310 | 0.907 | 34 %
United Kingdom | 0.193 | 0.430 | 45 %
Albania | 0.000 | 0.000 | –
Annex III = Annex II ÷ fossil share. Türkiye's mix is 58–65 % fossil, Georgia's ~20–25 % gas — the identity holds. Albania has no thermal plant and is listed at 0 in both: hydro is not what is taxed, gas is.
Two arguments that do not work
▪ No mark-up applies to electricity. The +10 / +20 / +30 % phase-in of IR recital 5 covers the deviation of individual installations from a national average, so it sits only in the Annex I goods tables. Annex III carries one column, with no year on it.
▪ Actual emissions are not available on this border. Annex IV §5 requires all five of: a PPA with the producer, a plant directly connected to the EU system (or demonstrated absence of congestion), ≤ 550 gCO₂/kWh, hourly firm nomination on allocated interconnection capacity, and monthly verification.
Sources: Regulation (EU) 2023/956, Annex IV §1(d), §4.2.1 and §5 · Commission Implementing Regulation (EU) 2025/2621 of 16 December 2025 (OJ L, 31.12.2025), recitals 3–8, Article 1(3)–(4), Annexes I–III — values sourced from the IEA · implied fossil shares cross-checked against Ember Türkiye Electricity Review and IEA Georgia energy mix.