## Slide 1
CBAM – Focus
→ CBAM:
a carbon price paid at the EU border. Every MWh entering the EU pays the ETS price on its deemed carbon — one direction only.
Calculation
CBAM (€/MWh) = EF (tCO₂e/MWh) × ETS price (€/tCO₂) × 100 %
EF
Annex III default — not the grid mix
ETS price
Observed 2024, then TYNDP 2024: 84 → 122 → 159 €/t
100 % from 2026
No phase-in: EU power has had no free allowances since 2013
Georgia's grid averages 0.102 tCO₂/MWh — its export default is 0.440, because the plant answering an export order is thermal.
The factor sets the levy, the levy sets what an export is worth · €2024 / MWh, Central EU price
Exporter | EF | 2026 | 2030 | 2040 | Net-back 2030 without → with | Year at the floor, 2040
Türkiye → BG / GR | 0.718 | 55 | 88 | 114 | 85 → 14 | 81 %
Georgia → RO | 0.440 | 33 | 54 | 70 | 83 → 33 | 35 %
Serbia | 1.041 | 79 | 127 | 165 | – | –
Ukraine | 0.907 | 69 | 111 | 144 | – | –
Moldova | 0.530 | 40 | 65 | 84 | – | –
EU reference | 0.612 | – | – | – | – | –
By 2030 the Turkish levy (88) meets the EU price itself (89). Georgia, at half the factor, keeps a margin.
Sources: Regulation (EU) 2023/956; Implementing Regulation (EU) 2025/2621 Annex III default factors; EU ETS observed 2024 and ENTSO-E TYNDP 2024 carbon price.